## Slide 1: Project 1 CO concentration Level prediction
8조 진형남, 박민수, 신명진, 장대근

## Slide 2
목차
Problem Statement
Exploration
Domain Exploration (Literature Review)
Data Exploration
Methods & Results
Overall Approach
Summary: Models & Results
Conclusion

## Slide 3
Problem Statement
Predict CO concentration levels from 16 gas sensor data
Given data

## Slide 4
Domain Exploration (1/2) by Literature Review
(General) In-Lab Mixed Gas Test Environment
*Ref.: Yonghui Xu, et al., “Research on a Mixed Gas Recognition and Concentration Detection Algorithm Based on a Metal Oxide Semiconductor Olfactory System
Sensor Array,” Sensors, 2018
① Mixed air injection ② Fresh air injection
① Mixed air injection
② Fresh air injection
Delayed sensor response due to:
Remaining gas in the chamber (before fully exhausted)
Sensor array structure
Sensor internal characteristics (∵ analog lowpass filter)
☞ 1) Need to align measured signals with reference CO
2) Need additional attributes reflecting abrupt changes
Reference
Measured

## Slide 5
Domain Exploration (2/2) by Literature Review
Nonlinearity in Cross-sensitivity characteristics & Mixed response
☞ Model should represent these nonlinearities!
TGS2600
*Ref.: Datasheets (Sensor specifications) of FIGARO TGS Series Sensors
*Ref.: Yonghui Xu, et al., “Research on a Mixed Gas Recognition and Concentration Detection Algorithm Based on a Metal Oxide Semiconductor Olfactory System Sensor
Array,” Sensors, 2018
“The response output of the sensor to the mixed gas is not equal to the sum of the responses of the sensor to the two target gases and has a nonlinear characteristic.”

## Slide 6
Data Exploration (1/3)
Cross-Correlation Analysis: ① Sensor Failure @ “s2” → Exclusion?
② Similar Sensors → Selection or Merge?
Sensor may be failed at this point!

## Slide 7
Data Exploration (2/3)
Need of Signal Shifts → 2000 samples shifted!
*Measured signal = Lowpass-filtered form of target signal
**Poor ability to track abrupt change in CO concentration level
→ Need additional information reflecting abrupt changes
Map to 0
Map to 310
Delayed
sensor
response
Unstabilized
region exists!
(e.g., “s9”)

## Slide 8
Data Exploration (3/3)
Need of Signal Conditioning → Zero-Phase Lowpass Filter Applied!
①
②
①
②
Min
Max
Impulsive noise exists!
<Raw>
<Filtered>
<Raw>
<Filtered>

## Slide 9
Overall Approach
Data cleaning
Signal conditioning
Signal shifting
Data
Preprocessing
Main Processing
Post Processing
Linear Regression
XGBoost
MLP
Nearest Mapping
Probabilistic Mapping (by Gaussian NB)
*Exclude “s2” col.
*Column selection & merge
*Lowpass filtering
*2000 samples shift
Pre-
knowledge
Best strategy
CNN

## Slide 10
Pre- & Post-processing (79.5 % MAE reduced w/ Linear Regression)
All raw data (Default)
“s2” exclusion
Filtering (fc=1Hz)
Data shift (2000 samples)
Shift&Filtering
40 %
decreases
(59.0→35.5)
66 %
decreases
(35.5→12.1)
Min-Max Clipping
Mapping to Nearest CO
Mapping to CO w/ maximum probability
0
533.33
...
*Gaussian Naive Bayes (NB) classifier
*Performance evaluated with linear regression (LR) model
*Performance evaluated with linear regression (LR) model

## Slide 11
Attribute (Column) Augmentation
Slope (1st derivative) of Each Attribute → Identify abrupt changes
Identify this region (abrupt change point) using the slope information
Slope
Differentiation
Zero-Phase Lowpass Filtering
Filtered
signal (X)
Differentiated X
(dX)
Filtered dX

## Slide 12
Summary: (Combined) Models & Results
Linear Regression (Best MAE = 12.1)
Test Score (MAE)
XGBoost (Best MAE = 53.5)
CNN (Best MAE = 6.9)
MLP (Best MAE = 6.0)
60.0
0
10.0
20.0
30.0
40.0
50.0
Raw model
Time shifts & Filtering
Nearest mapping
Probabilisticmapping
Hyperparameter tuning
Pre- & Post- processing
70.0
Raw model
Time shifts & Filtering
Probabilistic mapping
Hyperparameter tuning
Time shifts & Filtering
All combined
*All combined
Lowpass filtering
Time shifts
Attributes augmentation
Probabilistic mapping
Hyperparameter tuning

## Slide 13
Conclusion
Linear regression
Simple but powerful (∵ highly correlated data)
Limited performance (∵ only linear relationship)
XGBoost
Good for classification (than regression tasks)
Poor at extrapolation (depends on training set)
CNN
Good for data with spatial relationship
MLP - Achieved the best performance
Good for time-series prediction (w/ tabular data)
But too many parameters (∵ full connection)
*Ref.: Towards Data Science, “Why XGBoost Can’t Solve All Your Problems”
*Ref.: MachineLearningMastery, “When to use MLP, CNN, and RNN neural networks”
Different time shifts per sensors (columns)
Use CNN w/ spatial representation (e.g., spectrum)
Use RNN models - e.g., LSTM, Transformer
Ensemble model
“No Free Lunch”
Further Works
 | s1 | s11 | s13 | s15
Optimal Time Shift* | 4700 | 2700 | 2300 | 2200
*Calculated by the maximum cross-correlation
Data